PI3EQX7741ST

PI3EQX7741ST EVB Rev.A User Manual

by Noyes Mok

Introduction

Pericom’s PI3EQX7741ST is a low power high performance 5.0Gbps signal ReDriver designed for USB3.0 protocol. The device provides programmable Equalization (EQ) and De-Emphasis (DE) to optimize performance over a variety of physical mediums by reducing Inter-Symbol Interference (ISI)

The PI3EQX7741ST evaluation board (EVB) is designed to demonstrate the benefits, performance and key features of PI3EQX7741ST. This user manual describes the usage of this EVB and it will be divided into following sections:

- Overview

- Quick start

- Board Design information

    - PI3EQX7741ST EVB Schematic

    - PCB Layout

    - PCB Layout Reference

    - BOM List

Overview

Figure 1 is the block diagram of Pericom PI3EQX7741ST Evaluation board (EVB) and Figures 2(a) and (b) is the top and bottom view of EVB board. There is an USB3.0 Type-B Receptacle connector (JP6) which is used to connect PC’s USB3.0 port through a USB3.0 cable and the USB3.0 Type-A receptacle connector (JP7) is used to connect USB3.0 HDD or Hub through a USB3.0 cable. The EQ and DE setting on SW1 are used to select the equalization and de-emphasis level on PI3EQX7741ST. JP2 is used to enable receive detect function.

PI3EQX7741ST operation required +3.3V which was provided by the 3.3V LDO.

Figure 1, block diagram of PI3EQX7741ST EVB

Figure 2(a), top view of PI3EQX7741ST EVB        			Figure 2(b), bottom view of PI3EQX7741ST EVB

Quick Start

To start-up the PI3EQX7741ST EVB, complete the following steps:

- Check the head pin status and SW1 setting follow Table 1

- Connect the JP6 on EVB to PC’s USB3.0 port through a USB3.0 Type A to B cable.

- Plug the USB3.0 device into EVB USB Type-A connector JP7 through USB3.0 cable

Header pin is set as defaulted on EVB.

| Header pin # | Pin name | Switch status | Remark |
| --- | --- | --- | --- |
| JP2 | RxDet | Open | Enable Receive detect function |
| JP4 | EN_A# | Open | Channel A enable |
| JP5 | EN_B# | Open | Channel B enable |
| JP8 | VTH* | Open | Pull HIGH for normal operation |
| JP9 | VDD | Short | Use internal power from PC USB port |
| SW1 – 1 SW1 – 2 | DE_A | SW1 – 1 = ON SW1 – 2 = OFF | De-emphasis setting on channel A = 0dB |
| SW1 – 3 SW1 – 4 | EQ_A | SW1 – 3 = ON SW1 – 4 = OFF | Equalizer setting on channel A = 3dB |
| SW1 – 5 SW1 – 6 | DE_B | SW1 – 5 = ON SW1 – 6 = OFF | De-emphasis setting on channel B = 0dB |
| SW1 – 7 SW1 – 8 | EQ_B | SW1 – 7 = ON SW1 – 8 = OFF | Equalizer setting on channel B = 3dB |

Remark: *header pin VTH is connected to RES pin on PI3EQX7741ST

Table 1, Header pin settings for EVB (header pins location refers to Figure 4)

Figure 3, Connection of PI3EQX7741ST EVB

Detail Description

The functionality of header pins, switch are detail described in this section.

Functionality of Header Pins

| Header Pin | Header Pin Name | Pins on PI3EQX7741ST | Description |
| --- | --- | --- | --- |
| JP2 | RxDet | RxDet | Short = Receiver detect function disable Open = Receiver detect function ENABLE |
| JP4 | EN_A# | EN_A# | Short = Channel A disable Open = Channel A ENABLE |
| JP5 | EN_B# | EN_B# | Short = Channel B disable Open = Channel B ENABLE |
| JP8 | VTH* | RES | Reserved pin – MUST tie HIGH for normal operation |
| JP9 | VDD | VDD33 | Short = Use internal power Open = Use external 3.3V power |

VTH* is connected to RES pin on PI3EQX7741ST

Functionality of Switch (SW1)

| Switch - # | Pin on PI3EQX7741ST | Switch Status | Value |
| --- | --- | --- | --- |
| SW1 – 1 SW1 – 2 | DE_A | SW1 – 1 = ON, SW1 – 2 = OFF | 0dB |
|  |  | SW1 – 1 = OFF, SW1 – 2 = OFF | -3.5dB |
|  |  | SW1 – 1 = OFF, SW1 – 2 = ON | -6dB |
| SW1 – 3 SW1 – 4 | EQ_A | SW1 – 3 = ON, SW1 – 4 = OFF | 3dB |
|  |  | SW1 – 3 = OFF, SW1 – 4 = OFF | 6dB |
|  |  | SW1 – 3 = OFF, SW1 – 4 = ON | 9dB |
| SW1 – 5 SW1 – 6 | DE_B | SW1 – 5 = ON, SW1 – 6 = OFF | 0dB |
|  |  | SW1 – 5 = OFF, SW1 – 6 = OFF | -3.5dB |
|  |  | SW1 – 5 = OFF, SW1 – 6 = ON | -6dB |
| SW1 – 7 SW1 – 8 | EQ_B | SW1 – 7 = ON, SW1 – 8 = OFF | 3dB |
|  |  | SW1 – 7 = OFF, SW1 – 8 = OFF | 6dB |
|  |  | SW1 – 7 = OFF, SW1 – 8 = ON | 9dB |

Board Design Information:

  - PI3EQX7741ST EVB Schematic

- PCB Layout

Figure 4, Top view of PI3EQX7741ST EVB Layout

Figure 5, Bottom view of PI3EQX7741ST EVB Layout

- PCB Layout Requirements

- Stack Up:

| Layer # | Plane | Material Type | Thickness (mil) |
| --- | --- | --- | --- |
|  | Solder Mask |  | 0.4 |
| Layer 1 | Signal |  | 1.2 |
|  | Prepreg | FR4 1080 FR4 2216 | 7.3 |
| Layer 2 | GND |  | 1.2 |
|  | Core |  | 44 |
| Layer 3 | Power |  | 1.2 |
|  | Prepreg | FR4 2216 FR4 1080 | 7.3 |
| Layer 4 | Signal |  | 1.2 |
|  | Solder Mask |  | 0.4 |

- Isolation Spacing = 25 mil

- Width & Spacing (W/S) of 90Ω Differential Trace = 11 / 10 / 11 mil

- BOM List

| Item | Quantity | Reference | Description |
| --- | --- | --- | --- |
| 1 | 6 | C1, C2, C3, C8, C9, C10 | 0.1uF Capacitor |
| 2 | 4 | C4, C5, C6, C7 | 0.01uF Capacitor |
| 3 | 5 | EC1, EC2, EC3, EC4, EC5 | 22uF Capacitor |
| 4 | 1 | D1 | Green LED |
| 5 | 2 | JP1, JP3 | 3 x 1 Header Pin |
| 6 | 5 | JP2, JP4, JP5, JP8, JP9 | 2X1 Header Pin |
| 7 | 1 | JP6 | USB3.0 Type B Receptacle connector |
| 8 | 1 | JP7 | USB3.0 Type A Receptacle connector |
| 9 | 8 | R1, R2, R3, R4, R5, R6, R7, R8 | 10kΩ Resistor |
| 10 | 1 | R9 | NP |
| 11 | 1 | R10 | 0Ω Resistor |
| 12 | 1 | R11 | 510Ω Resistor |
| 13 | 1 | SW1 | SPDT switch |
| 14 | 1 | U1 | PI3EQX7741ST |
| 15 | 1 | U2 | CJ1117 – 3.3V |

# Text boxes

JP7

JP7

USB3.0

Type A Receptacle

VDD

GND

JP6

USB3.0

Type B

Receptacle

JP7

Header pin for external power supply use

SW1

3.3V LDO

SW1

PI3EQX7741ST

JP8

JP2

DE_A/B

RX±

JP5

USB 3.0 Type B Receptacle

EQ_A/B

JP6

USB3.0

Type A Receptacle

EVB plug-into PC USB port through USB3.0 cable

USB3.0 device

JP6

PI3EQX7741ST EVB

PC with USB3.0 host

USB 3.0 Type A Receptacle

JP4

JP9

BO±

USB3.0

Type B

Receptacle

TX±

Device plug-into EVB through USB3.0 cable

Device

AO±

AI±

3.3V LDO

Switch for EQ and DE selection

D±

HOST

RxDET

JP2

BI±