PI3VDP12412ZHE

Demo Board Rev.B User Manual
by Ada Yip

Table of Contents

1	Introduction	2

2	Overview	2

3	Quick Start	3

4	Circuit Description	4

4.1	Port Selection	4

4.2	3.3V Power Supply	4

4.3	Power Saving Mode	4

5	Relative References	5

6	Appendix A: Demo Board Schematic	5

# Introduction

PI3VDP12412 is a 4-lane mux or de-mux DP1.2 switch for source as well as sink applications. This user manual describes the components and the usage of PI3VDP12412ZHE Demo Board Rev.B for source application.

# Overview

Figure 1 is the block diagram of Pericom PI3VDP12412ZHE demo board and figure 2 shows the top view of the demo board. For source application evaluation, two DP plug connector (J101-2) on PI3VDP12412ZHE demo board are used for plugging DP source devices, such as motherboard and graphic card. A DP cable can be connected between a DP receptacle connector (J103) on the demo board and a DP sink device, such as DP monitor. +5V DC can be employed to the demo board via a mini USB female connector (J104). Through a 3.3V regulator (U102), PI3VDP12412 on the demo board can then be powered up.  Port selections of PI3VDP12412 can be adjusted via a SPDT switch (SW101).

Figure 1: Block Diagram of PI3VDP12412ZHE Demo Board Rev.B

Figure 2: Top View of PI3VDP12412ZHE Demo Board

# Quick Start

To start-up the PI3VDP12412ZHE demo board rev.B, complete the following steps:

- Keep pins 1 and 8 of SPDT switch SW101 open to set OE pin to high;

- Leave pins 2 and 7, and 3 and 6 of SPDT switch SW101 open to select Port B of PI3VDP12412ZHE;

- Supply 5V to demo board from mini USB connector at J104;

- Plug DP input connector J102 on demo board to a source device, e.g. DP motherboard;

- Connect a sink device, e.g. DP monitor, to DP output connector at J103.

Figure 3: Layout of PI3VDP12412ZHE Demo Board

# Circuit Description

# Port Selection

PI3VDP12412ZHE offers two control pins for selecting ports for high-speed signals, HPD and AUX.

| GPU_SEL (Pins 2 and 7 of SW101) | AUX_HPD_SEL (Pins 3 and 6 of SW101) | Function |
| --- | --- | --- |
| Low (Short) | Low (Short) | Port A active for all channels |
| Low (Short) | High (Open) | Port A for HS, Port B for HPD/AUX |
| High (Open) | Low (Short) | Port B for HS, Port A for HPD/AUX |
| High (Open) | High (Open) | Port B active for all channels |

Table 1: Port Selection of PI3VDP12412ZHE Demo Board Rev.B

# 3.3V Power Supply

By shorting header JP101 on PI3VDP12412ZHE demo board rev.B, VDD of PI3VDP12412ZHE can be employed through two methods as below:

- A +3V3_USB power rail via mini-USB adaptor connected to mini USB2.0 connector J104 and 3.3V regulator U102;

- A +3V3_A/B power rail via any source connected to input DP connector J101/2.

Figure 4: Power Circuit of PI3VDP12412ZHE Demo Board Rev.B

# Power Saving Mode

PI3VDP12412ZHE can enter power saving mode by setting OE pin to low voltage level.

| OE | I/O Pins of PI3VDP12412 | Pins 1 and 8 of SW101 |
| --- | --- | --- |
| H | Normal Mode | Open |
| L | Power Saving Mode | Short |

Table 2: OE Setting of PI3VDP12412ZHE Demo Board Rev.B

# Relative References

- High-Definition Multimedia Interface Specification Version 1.4, HDMI Licensing, LLC, June 5, 2009

- High-Definition Multimedia Interface Compliance Test Specification Version 1.4a, HDMI Licensing, LLC, 2010/03/04

# Appendix A: Demo Board Schematic

For clearer view of schematic diagram, please click the PDF file icon on the right.

# Text boxes

DP Output Connector

DP Input Connectors

J101

Output Port

J102

Port B

J104

U101

+5V

SPDT Switch

SW101

U102

Port A

Mini USB Connector

+3V3_USB

3.3V Regulator

J103

PI3VDP12412

Short