PI3DPX1203

Sink Demo Board Rev.A User Manual
by Ada Yip

Table of Contents

1	Introduction	2

2	Overview	2

3	Quick Start	3

4	Circuit Description	4

4.1	Equalization Setting	4

4.2	Output Linearity Setting	5

4.3	Flat Gain Setting	5

4.4	I2C_MODE/_RESET# Setting	5

4.5	Programming Mode	6

4.6	5V/3.3V Power Supply	6

4.7	Power Saving Mode	7

5	References	7

6	Appendix A: Demo Board Schematic	8

# Introduction

PI3DPX1203 DP1.3 linear re-driver can be employed in source as well as sink applications. This user manual describes the components and the usage of PI3DPX1203 Sink Demo Board Rev.A. Output swing linearity and gain flatness can be tuned in order to recover input DP signal as desired.

# Overview

Figure 1 is the block diagram of Pericom PI3DPX1203 sink demo board and figure 2 shows the top view of the demo board. One DP plug connector (J101) on PI3DPX1203 demo board is used for plugging a source device, such as a DP graphic card. A DP cable can be connected between a DP receptacle connector (J102) on the demo board and a sink device, such as a DP monitor. +5V DC can be employed to the demo board via a mini USB female connector (J103) and/or the source device. Through a 3.3V regulator (U102), PI3DPX1203 on the demo board can then be powered up.

I2C mode is enabled via ON/OFF switch (SW102) if the data stored in the I2C bus is used to program PI3DPX1203. I2C address can be set via ON/OFF switch (SW101) if I2C mode of PI3DPX1203 is selected. Equalization, output linearity and flat gain settings of PI3DPX1203 can be adjusted via the same ON/OFF switch (SW101).

Figure 1: Block Diagram of PI3DPX1203 Sink Demo Board Rev.A

Figure 2: Top View of PI3DPX1203 Sink Demo Board Rev.A

# Quick Start

To start-up the PI3DPX1203 sink demo board Rev.A for evaluating PI3DPX1203, complete the following steps:

- Keep pins 7 and 8 of SW101 switch open so as to set the output linearity of PI3DPX1203 to 1000mV;

- Leave pin 2 of SW101 switch open while short pins 1 and 16 to set flat gain of PI3DPX1203 to 0dB;

- Short pins 3 and 6 of SW102 switch and leave pin 2 open so that PI3DPX1203 is set to pin control mode;

- Short pins 3/4/5/6 to 14/13/12/11 of SW101 switch of PI3DPX1203, respectively, to set equalization to 1.8dB at 6Gbps;

- Short JP103 header pin to allow 3.3V from a source device feeding current to PI3DPX1203, or short JP106 header pin and connect a USB3 cable to J103 USB3 receptacle connector to feed 5V to PI3DPX1203 sink demo board;

- Connect a source device, e.g. graphic card, to J101 DP receptacle connector via a DP cable;

- Plug J102 DP plug connector to a sink device, e.g. DP monitor.

# Circuit Description

# Equalization Setting

PI3DPX1203 offers several equalization values for covering designs with short and long input PCB traces or cables.  The table below provides a reference of EQ settings with various input FR4 trace length.

| EQ3 | EQ2 | EQ1 | EQ0 | 6Gbps Input | Input FR4 Trace (in) |
| --- | --- | --- | --- | --- | --- |
| 0 | 0 | 0 | 0 | 1.8 dB | 2” – 10” |
| 0 | 0 | 0 | 1 | 2.1 dB |  |
| 0 | 0 | 1 | 0 | 2.5 dB |  |
| 0 | 0 | 1 | 1 | 2.9 dB |  |
| 0 | 1 | 0 | 0 | 3.2 dB |  |
| 0 | 1 | 0 | 1 | 3.6 dB |  |
| 0 | 1 | 1 | 0 | 4.0 dB |  |
| 0 | 1 | 1 | 1 | 4.3 dB |  |
| 1 | 0 | 0 | 0 | 4.7 dB |  |
| 1 | 0 | 0 | 1 | 5.1 dB | 10” – 24” |
| 1 | 0 | 1 | 0 | 5.4 dB |  |
| 1 | 0 | 1 | 1 | 5.8 dB |  |
| 1 | 1 | 0 | 0 | 6.1 dB |  |
| 1 | 1 | 0 | 1 | 6.4 dB |  |
| 1 | 1 | 1 | 0 | 6.7 dB |  |
| 1 | 1 | 1 | 1 | 7.0 dB |  |

Table 1: EQ Setting of PI3DPX1203 Sink Demo Board Rev.A

Figure 3: SW101 on PI3DPX1203 Sink Demo Board Rev.A

# Output Linearity Setting

PI3DPX1203 offers four steps of linearity setting in response to the input amplitude changes. To maintain linearity with respect to the input swing, 1000mV should be chosen.

| SW1 | SW0 | Differential Swing |
| --- | --- | --- |
| 0 | 0 | 700 mV |
| 0 | 1 | 800 mV |
| 1 | 0 | 900 mV |
| 1 | 1 | 1000 mV |

Table 2: Output Linearity of PI3DPX1203 Sink Demo Board Rev.A

# Flat Gain Setting

Depending on the output trace length, different flat gain values may be picked for individual designs. For supporting long output cable, maximum flat gain should be set.

| FG1 | FG0 | Gain |
| --- | --- | --- |
| 0 | 0 | -4 dB |
| 0 | 1 | -2 dB |
| 1 | 0 | 0 dB |
| 1 | 1 | 2 dB |

Table 3: Flat Gain of PI3DPX1203 Sink Demo Board Rev.A

# I2C_MODE/_RESET# Setting

When tying multiple PI3DPX1203 devices to SCL and SDA buses, individual address should be set for each device via AD[3:0] such that its configuration can be loaded from the EEPROM properly. The address of the first device in the sequence must be set to 0x00h. Subsequent devices must follow the address order listed below.

- U1: AD[3:0] = 0000 = 0x00h

- U2: AD[3:0] = 0001 = 0x10h

- U3: AD[3:0] = 0010 = 0x20h

- U4: AD[3:0] = 0011 = 0x30h

I2C_RESET# and I2C_DONE must be daisy-chained from one device to the next in the following sequence so that EEPROM is read by one device at a time.

- Tie I2C_DONE of U1 to I2C_RESET# of U2

- Tie I2C_DONE of U2 to I2C_RESET# of U3

- Tie I2C_DONE of U3 to I2C_RESET# of U4

- (Optional) Tie I2C_DONE of U4 to an LED to show the devices have been loaded successfully

# Programming Mode

ENI2C (pin 21) of PI3DPX1203 is used to select between I2C or Pin control mode. It is set via SW102 switch. I2C address at pins 39-42 of PI3DPX1203 is set via SW101 switch. The pins are shared with EQ pins.

Figure 4: SW102 on PI3DPX1203 Sink Demo Board Rev.A

| ENI2C | SW102 | Programming Mode |
| --- | --- | --- |
| L | Short pins 3 and 6; Open pins 2 and 7 | Pin Control Mode |
| H | Short pins 2 and 7; Open pins 3 and 6 | I2C Control Mode |

Table 4: ENI2C Setting of PI3DPX1203 Sink Demo Board Rev.A

# 5V/3.3V Power Supply

3.3V on PI3DPX1203 sink demo board rev.A can be fed through three methods.

- Any source connected to input DP connector J101 via +3V3_SRC power rail providing that JP103 header pin is shorted;

- USB3 cable connected to USB3 receptacle connector J103 via +5V_USB power rail if JP106 header pin is shorted;

- External power supply via JP101 header pin with JP102 as GND reference.

Figure 5: Power Circuit of PI3DPX1203 Sink Demo Board Rev.A

# Power Saving Mode

PI3DPX1203 can enter power saving mode by setting PRSNT# pin to high voltage level. In the schematic, PRSNT# pin is controlled by VCC of PI3DPX1203.

Figure 6: PRSNT# Circuit of PI3DPX1203 Sink Demo Board Rev.A

Alternatively, PRSNT# can be selected via switch SW101.

| PRSNT# | Pins 4 and 5 of SW102 | Output Main Link of PI3DPX1203 |
| --- | --- | --- |
| L | Short | Normal Mode |
| H | Open | Power Saving Mode |

Table 5: PRSNT# Setting of PI3DPX1203 Sink Demo Board Rev.A

# References

- VESA DisplayPort Standard Version 1 Revision 2a, Video Electronics Standards Association, January 5, 2010

- VESA DisplayPort PHY Compliance Test Specification, Version 1.2b, Video Electronics Standards Association, November 26, 2012

# Appendix A: Demo Board Schematic

For clearer view of schematic diagram, please click the PDF file icon on the right.

# Text boxes

PI3DPX1203

J102

USB3 Connector

Input Port

U102

SW102

ON/OFF Switches

J101

DP Input Connector

DP Output Connector

Output Port

U101

+3V3_SRC

J103

+5V_USB

+3V3_USB

SW101

DC-DC Convertor

U105

Power Distribution Switch