PI3HDMI2410

2-Layer Demo Board Rev.A User Manual

by Ada Yip

Introduction

Pericom’s PI3HDMI2410 is a 4:1 HDMI switch with I2C control specifically for Sink Application. All HDMI control settings are through I2C bus to maximize design flexibility and reduce peripheral components. PI3HDMI2410 offers a selection of passive switch or active DDC signal buffer for optimizing data transmission in long trace or cable applications. HPD polarity is freely set by user.

- Overview

- Quick Start

- Control Register Description

- Test Result

Overview

Figure 1 is the block diagram of Pericom PI3HDMI2410 Demo Board and Figures 2a and b show the top and bottom views of the demo board. There are four HDMI Type A receptacle connectors (P1, 3-5), which are used to connect to the HDMI source devices, such as DVD players. The HDMI Type A plug connector (P2) is used to connect to the HDMI sink device, such as HDTV. The demo board is powered up by a +5V DC from mini USB female connector (J1) and a 3.3V regulator (U2).

Enable Pin (/OE), I2C Address (A0-1), VIL selection of DDC buffer (VSEL), and DDC Open Drain Output Setting (WP_SET) can be controlled using header pins JP2-6 on demo board. I2C registers of PI3HDMI2410 can be changed via I2C bus at header pin JP7.

Figure 1: Block Diagram of PI3HDMI2410 Demo Board

Figure 2a: Top View of PI3HDMI2410 Demo Board

Figure 2b: Bottom View of PI3HDMI2410 Demo Board

Quick Start

To start up the PI3HDMI2410 Demo Board, follow the steps below:

- Short /OE pin to GND in order to enable PI3HDMI2410 using header pin JP2;

- Set I2C Address bits, A0 and A1, to low level via header pins JP3 and 5  to set I2C Address to A8;

- Short VIL of DDC buffer to GND at header pin JP4 to set VIL to 0.5V (0.45V and 0.6V VIL are also available);

- Short WP_SET to GND at header pin JP6 to set B1b[1] of I2C register to indicate the presence of any +5V pin of HDMI input connectors;

- Connect an I2C Bus Host Adaptor to SCL_CTL, SDA_CTL and GND pins at header pin JP7;

- Supply 5V to demo board from mini USB Connector at J1;

- Connect Sources, e.g. DVD players, to HDMI Input Connectors at P1 and P3-5;

- Connect Sink, e.g. HDTV, to HDMI Output Connector at P2;

- Through I2C Address A8, write the following data into Bytes 0 and 1 to enable particular HDMI input port and turn on DDC buffer:

- Byte 0 = 20, Byte 1 = 45 for Port 1

- Byte 0 = 60, Byte 1 = 49 for Port 2

- Byte 0 = A0, Byte 1 = 51 for Port 3

- Byte 0 = E0, Byte 1 = 61 for Port 4

Figure 3: Layout of PI3HDMI2410 Demo Board (Top View)

Control Register Description

All switch control settings through I2C bus are described below.

  - HDMI input port is selected through Byte 0 Bits 6-7.

| Data Byte | Bit 7 | Bit 6 | Setting |
| --- | --- | --- | --- |
| 0 | 0 | 0 | Port A |
|  | 0 | 1 | Port B |
|  | 1 | 0 | Port C |
|  | 1 | 1 | Port D |

- HPD polarity can be controlled by Byte 0 Bit 5.

| Data Byte | Bit 5 | Setting |
| --- | --- | --- |
| 0 | 0 | Inverted => HPD_x = /HPD_SINK |
|  | 1 | Non Inverted => HPD_x = HPD_SINK |

- HPD inputs can be selected to follow external setting on HPD_SINK pin or I2C register Byte 0 Bits 0-3.

| Data Byte | Bit 4 | Setting |
| --- | --- | --- |
| 0 | 0 | HPD input follows external setting on HPD_SINK |
|  | 1 | HPD input follows B0b[3:0] |

- Provided that HPD input selection in Byte 0 Bit 4 is set to use B0b[3:0], HPD input D/C/B/A can be controlled by Byte 0 Bit 4/3/2/1, respectively.

| Data Byte | Bit 3/2/1/0 | Setting |
| --- | --- | --- |
| 0 | 0 | HPD D/C/B/A = Low |
|  | 1 | HPD D/C/B/A = High |

- HPD output stage offers a selection of open drain and output buffer in Byte 1 Bit 7.

| Data Byte | Bit 7 | Setting |
| --- | --- | --- |
| 1 | 0 | Open Drain |
|  | 1 | Output Buffer |

- TMDS output can be enabled by hardware, /OE, and software, I2C resister Byte 1 Bit 6. Assuming that /OE is pulled low externally, B1b6 setting is as below.

| Data Byte | Bit 6 | Setting |
| --- | --- | --- |
| 1 | 0 | Output Disable; Power Down Mode |
|  | 1 | Output Enable |

- DDC channel offers a selection of passive switch and active switch buffer. To minimize the DDC capacitance, active switch buffer is recommended for long trace application.

| Data Byte | Bit 0 | Setting |
| --- | --- | --- |
| 1 | 0 | Passive Switch |
|  | 1 | Active Switch Buffer |

Test Result

Few Sink test items specified in HDMI Compliance Test Spec are performed here.

- Test ID 8-4: TMDS – Termination Voltage

Termination voltage is tested at HDMI input connector P1 when demo board is connected to HDTV and both demo board and HDTV are powered up.

| Output | Vterm | Spec | Units |
| --- | --- | --- | --- |
|  |  | Min | Max |  |
| D2+ | 3.26 | 3.125 | 3.475 | V |
| D2- | 3.26 | 3.125 | 3.475 | V |
| D1+ | 3.26 | 3.125 | 3.475 | V |
| D1- | 3.26 | 3.125 | 3.475 | V |
| D0+ | 3.26 | 3.125 | 3.475 | V |
| D0- | 3.26 | 3.125 | 3.475 | V |
| CLK+ | 3.26 | 3.125 | 3.475 | V |
| CLK- | 3.26 | 3.125 | 3.475 | V |

- Test ID 8-8: TMDS – Differential Impedance

TDR of all input TMDS lines are measured when PI3HDMI2410 is powered off.

| HDMI Input Port | Through Impedance | D2 | D1 | D0 | CLK | Spec | Units |
| --- | --- | --- | --- | --- | --- | --- | --- |
|  |  |  |  |  |  | Min | Max |  |
| P1 | Min | 84(1) | 84(1) | 86 | 87 | 85 | 115 | ( |
|  | Max | 110 | 106 | 106 | 108 | 85 | 115 | ( |
| P3 | Min | 91 | 89 | 89 | 89 | 85 | 115 | ( |
|  | Max | 112 | 106 | 110 | 108 | 85 | 115 | ( |
| P4 | Min | 92 | 89 | 89 | 89 | 85 | 115 | ( |
|  | Max | 113 | 107 | 109 | 109 | 85 | 115 | ( |
| P5 | Min | 87 | 89 | 89 | 87 | 85 | 115 | ( |
|  | Max | 108 | 105 | 107 | 108 | 85 | 115 | ( |

(1) A single excursion is permitted out to a max/min of 100Ω±25% and of a duration less than 250ps.

Figure 4a: D2 TDR of HDMI Port P1

Figure 4b: D1 TDR of HDMI Port P1

Figure 4c: D0 TDR of HDMI Port P1

Figure 4d: CLK TDR of HDMI Port P1

Figure 5a: D2 TDR of HDMI Port P3

Figure 5b: D1 TDR of HDMI Port P3

Figure 5c: D0 TDR of HDMI Port P3

Figure 5d: CLK TDR of HDMI Port P3

Figure 6a: D2 TDR of HDMI Port P4

Figure 6b: D1 TDR of HDMI Port P4

Figure 6c: D0 TDR of HDMI Port P4

Figure 6d: CLK TDR of HDMI Port P4

Figure 7a: D2 TDR of HDMI Port P5

Figure 7b: D1 TDR of HDMI Port P5

Figure 7c: D0 TDR of HDMI Port P5

Figure 7d: CLK TDR of HDMI Port P5

- Test ID 8-10: HPD Output Voltage

DC voltage level of HPD pin at input HDMI connector P1 is tested when PI3HDMI2410 is powered up.

| Parameter | DUT Power | P_5V | VHPD | Spec | Units |
| --- | --- | --- | --- | --- | --- |
|  |  |  |  | Min | Max |  |
| VHPD_L | Off | 0.0V | 0.0 | 0.0 | 0.4 | V |
|  | On | 0.0V | 0.0 | 0.0 | 0.4 | V |
| VHPD_H | On | 4.8V | 4.78 | 2.4 | 5.3 | V |
|  | On | 5.3V | 5.08 | 2.4 | 5.3 | V |

EDID emulator is attached to PI3HDMI2410 output to model Sink device when performing the test.

- Test ID 8-11: HPD Output Resistance

HPD output resistance is measured by putting a 10kΩ resistor at HPD pin of input HDMI connector P1.

| Parameter | Data | Spec | Units |
| --- | --- | --- | --- |
|  |  | Min | Max |  |
| VA | 5.00 | NA | NA | V |
| VB | 4.55 | NA | NA | V |
| ZHPD | 989 | 800 | 1200 | Ω |

ZHPD = (VA/VB – 1) * 10,000

EDID emulator is attached to PI3HDMI2410 output to model Sink device when performing the test.

- Test ID 8-12: +5V Power Max Current

Power consumption drawn by Sink is measured at +5V power pin when DUT is in ON and OFF states.

| Test Condition | +5V Power Pin | Max Spec | Units |
| --- | --- | --- | --- |
|  | 4.9V | 5.1V |  |  |
| DUT is Powered On | 0.06 | 0.09 | 10 | mA |
| DUT is Powered Off | 0.16 | 0.17 | 50 | mA |

EDID emulator is attached to PI3HDMI2410 output to model Sink device when performing the test.

- Current Consumption of PI3HDMI2410

IDD current consumed by PI3HDMI2410 is measured at VDD pin when all outputs are enabled by /OE pin.

| Test Condition | -40C | 25C | 90C | Units |
| --- | --- | --- | --- | --- |
| VDD = 3.6V | 5.203 | 5.096 | 5.182 | mA |

- ESD Immunity Test

(8kV ESD Contact Test of 10-time contact is performed at each pin and shielding ground of each input/output connector, P1-5, of PI3HDMI2410 demo board based on IEC61000-4-2 standard. PI3HDMI2410 is tested using DVD players and 1080pHDTV afterwards. One resolution of 1080p/60Hz is checked.

| Port | Functionality |
| --- | --- |
|  | Video | Audio |
| Port A (P1) | Pass | Pass |
| Port B (P3) | Pass | Pass |
| Port C (P4) | Pass | Pass |
| Port D (P5) | Pass | Pass |
| Output Port (P2) | Pass | Pass |

Appendix A: Test Equipments

For Sink Test

- Fluke Multimeter

- HP Power Supply

- SMA Matching Cables

- HDMI-SMA Test Fixture

- 2m 28AWG HDMI Cable

- 12” SMA Cable

- SMA-to-SMA Adaptor

- USB Adaptor

For ESD Immunity Test

  - KIKUSUI Electrostatic Discharge Simulator (Model#: KES4021)

  - IEC CR Unit (Model#: NF002607)

  - Contact Discharge Tip (Model#: CT21-KES)

  - Sony BDP-S300 DVD Player

  - Samsung BD-P1000 DVD Player

  - DELL 2408WFPb Monitor

  - 2/3m 28AWG HDMI Cable

  - USB Adaptor

Appendix B: PI3HDMI2410 Demo Board Schematic

For clearer view of schematic diagram, please click the PDF file icon on the right.

Appendix C: 2-layer PCB Reference Data

Appendix D: BOM List

| Item | Quantity | Reference | Description |
| --- | --- | --- | --- |
| 1 | 6 | C1, C2, C3, C4, C5, C6 | 10nF Capacitor |
| 2 | 2 | C7, C9 | 22uF Capacitor |
| 3 | 2 | C8, C10 | 1uF Capacitor |
| 4 | 5 | D1, D2, D3, D4, D5, D10 | B0520LW Schottky Rectifier |
| 5 | 4 | D6, D7, D8, D9 | LED |
| 6 | 6 | JP2, JP3, JP4, JP5, JP6, JP7 | 3-Pin Headers |
| 7 | 2 | JP1-1, JP1-2 | 2-Pin Headers |
| 8 | 1 | J1 | Mini USB Female Connector |
| 9 | 4 | P1, P3, P4, P5 | HDMI Type A Receptacle Connector |
| 10 | 1 | P2 | HDMI Type A Plug Connector |
| 11 | 10 | R1, R7, R8, R11, R12, R13, R14, R19, R20, R21 | 1kΩ Resistor |
| 12 | 8 | R2, R3, R5, R6, R9, R10, R17, R18 | 47kΩ Resistor |
| 13 | 1 | R4 | 100kΩ Resistor |
| 14 | 1 | R15 | NOT POPULATED |
| 15 | 1 | R16 | 0Ω Resistor |
| 16 | 16 | R22, R23, R24, R25, R26, R27, R28, R29, R30, R31, R32, R33, R34, R35, R36, R37 | 620Ω Resistor |
| 17 | 1 | U1 | PI3HDMI2410 |
| 18 | 1 | U2 | 1117 3.3V Regulator |

# Text boxes

HDMI Input Connectors

P1

P3

Header Pins for Control Pins

PI3HDMI2410

JP7

P2

HDMI Output Connector

P5

P4

3.3V

Regulator

J1

Mini USB Connector

Header Pins for I2C Bus

Input Port D

Input Port C

Input Port A

Input Port B

U2

JP2-6