PI3HDMI511

PI3HDMI511 HDMI Application Information

Table of Contents

1	Introduction	2

2	External Component Requirements	2

2.1	AC Coupling Capacitors on Output Main Link	3

2.2	Pull-up Resistors on DDC Channel	3

2.3	Pull-up Resistor on HPD Channel	3

3	Layout Design Guideline	3

4	References	3

# Introduction

PI3HDMI511 is an HDMI 1.4 re-driver for source application. It can re-drive TMDS signals coming from dual-mode DP source or HDMI source. External components in typical application circuit and layout guideline are described in this application information.

# External Component Requirements

PI3HDMI511 is designed to accept AC-coupled as well as DC-coupled main link signals.

Figure 1: PI3HDMI511 HDMI Source Application

# AC Coupling Capacitors on Output Main Link

For dual-mode DP source, AC coupling capacitors should be placed before where TMDS signal pins enter PI3HDMI511 if signals from the dual-mode DP source are DC coupled.

# Pull-up Resistors on DDC Channel

Each of SCL and SDA is pulled up to 3.3V via a 20kΩ resistor to create a high voltage level for dual-mode DP source. The 2kΩ pull-ups to 5V are the requirement of HDMI Specification Version 1.4. As 5V-to-3.3V level shifter is implemented in the design, external FET is not required.

# Pull-up Resistor on HPD Channel

As HPD_SRC of PI3HDMI511 is an open drain buffer design, external pull-up should be implemented.

# Layout Design Guideline

Layout guideline especially for high-speed transmission is critical. Please refer to PIxxxx High Speed Layout Guideline, AN345, for detailed recommendations.

# References

- VESA DisplayPort Standard Version 1 Revision 2, Video Electronics Standards Association, January 5, 2010

- VESA DisplayPort Dual-Mode Standard Version 1, Video Electronics Standards Association, February 10, 2012

- VESA DisplayPort Interoperability Guideline Version 1.1a, Video Electronics Standards Association, February 5, 2009

- High-Definition Multimedia Interface Specification Version 1.4, HDMI Licensing, LLC, June 5, 2009

- PCI Express Board Design Guidelines Draft, Intel Corporation, June 2003