PI3HDX1204E

DP-to-HDMI Demo Board Rev.A User Manual
by Ada Yip

Table of Contents

1	Introduction	2

2	Overview	2

3	Quick Start	3

4	Circuit Description	4

4.1	Equalization Setting	4

4.2	Flat Gain Setting	5

4.3	I2C_MODE/_RESET# Setting	5

4.4	Programming Mode	6

4.5	5V/3.3V Power Supply	6

4.6	Power Saving Mode	7

5	References	7

6	Appendix A: Demo Board Schematic	8

# Introduction

PI3HDX1204E HDMI2.0 linear re-driver can be employed in source, cable as well as sink applications. PI3HDX1204E accepts dual-mode DP input and handles level shifting for DP++-to-HDMI application. This user manual describes the components and the usage of PI3HDX1204E Demo Board Rev.A.

# Overview

Figure 1 is the block diagram of Pericom PI3HDX1204E demo board and figure 2 shows the top view of the demo board. One DP plug connector (J101) on PI3HDX1204E demo board is used for plugging to a source device, such as a graphic card. An HDMI receptacle connector (J102) on the demo board can be connected to a sink device, such as HDTV, through an HDMI cable. +5V DC can be employed to the demo board via a USB3 receptacle connector (J103). Through a DC-DC convertor (U102), PI3HDX1204E on the demo board can then be powered up.

I2C mode is enabled via ON/OFF switch (SW101) if the data stored in the I2C bus is used to program PI3HDX1204E. I2C address can be set via the ON/OFF switch if I2C mode of PI3HDX1204E is selected. Equalization and flat gain settings of PI3HDX1204E can be adjusted via the same ON/OFF switch.

Figure 1: Block Diagram of PI3HDX1204E DP-to-HDMI Demo Board Rev.A

Figure 2: Top View of PI3HDX1204E DP-to-HDMI Demo Board Rev.A

# Quick Start

To start-up the PI3HDX1204E DP-to-HDMI demo board Rev.A, complete the following steps:

- Short JP103 header pin to connect I2C_DONE pin of PI3HDX1204E to an LED for reflecting if an external EEPROM is loaded;

- Short pins 7 and 10 of SW101 switch while keeping pin 6 open so that PI3HDX1204E is programmed to pin control mode;

- Short pins 3/4/5 to 14/13/12 of SW101 switch, respectively, to set equalization to 4dB at 6Gbps;

- Leave pin 2 of SW101 switch open and short pins 1 to 16 so as to set the gain flatness of PI3HDX1204E to 0.5dB;

- Connect a USB3 cable to J103 USB3 receptacle to feed 5V to PI3HDX1204E demo board;

- Plug J101 DP plug connector to a source device, e.g. graphic card;

- Connect a sink device, e.g. HDMI monitor, to J102 HDMI receptacle connector via an HDMI cable.

# Circuit Description

# Equalization Setting

PI3HDX1204E offers several equalization values for covering designs with short and long input PCB traces or cables.  The table below provides a reference of EQ settings with various input FR4 trace length.

| EQ3 | EQ2 | EQ1 | 6Gbps Input | Input FR4 Trace |
| --- | --- | --- | --- | --- |
| 0 | 0 | 0 | 4.0 dB | 5” – 10” |
| 0 | 0 | 1 | 4.7 dB |  |
| 0 | 1 | 0 | 5.5 dB | 10” – 20” |
| 0 | 1 | 1 | 6.2 dB |  |
| 1 | 0 | 0 | 6.6 dB |  |
| 1 | 0 | 0 | 6.9 dB |  |
| 1 | 0 | 1 | 7.6 dB | 20” – 25” |
| 1 | 1 | 0 | 8.2 dB |  |
| 1 | 1 | 1 | 8.9 dB |  |

Table 1: EQ Setting of PI3HDX1204E DP-to-HDMI Demo Board Rev.A

Figure 3: SW101 on PI3HDX1204E DP-to-HDMI Demo Board Rev.A

# Flat Gain Setting

Depending on the output trace length, different flat gain values may be picked for individual designs. For supporting long output cable, larger flat gain should be set.

| FG1 | FG0 | Gain |
| --- | --- | --- |
| 0 | 0 | -3.5 dB |
| 0 | 1 | -1.5 dB |
| 1 | 0 | +0.5 dB |
| 1 | 1 | +2.5 dB |

Table 2: Flat Gain of PI3HDX1204E DP-to-HDMI Demo Board Rev.A

# I2C_MODE/_RESET# Setting

When tying multiple PI3HDX1204E devices to SCL and SDA buses, individual address should be set for each device via AD[3:0] such that its configuration can be loaded from the EEPROM properly. The address of the first device in the sequence must be set to 0x00h. Subsequent devices must follow the address order listed below.

- U1: AD[3:0] = 0000 = 0x00h

- U2: AD[3:0] = 0001 = 0x10h

- U3: AD[3:0] = 0010 = 0x20h

- U4: AD[3:0] = 0011 = 0x30h

I2C_RESET# and I2C_DONE must be daisy-chained from one device to the next in the following sequence so that EEPROM is read by one device at a time.

- Tie I2C_DONE of U1 to I2C_RESET# of U2

- Tie I2C_DONE of U2 to I2C_RESET# of U3

- Tie I2C_DONE of U3 to I2C_RESET# of U4

- (Optional) Tie I2C_DONE of U4 to an LED to show the devices have been loaded successfully

# Programming Mode

ENI2C (pin 15) of PI3HDX1204E is used to select between I2C or Pin control mode. It is set via SW101 switch. I2C address at pins 30-2 of PI3HDX1204E is set via SW101 switch. The pins are shared with EQ pins.

| ENI2C | SW101 | Programming Mode |
| --- | --- | --- |
| L | Short pins 7 and 10; Open pins 6 and 11 | Pin Control Mode |
| H | Short pins 6 and 11; Open pins 7 and 10 | I2C Control Mode |

Table 3: ENI2C Setting of PI3HDX1204E DP-to-HDMI Demo Board Rev.A

# 5V/3.3V Power Supply

5V on PI3HDX1204E demo board rev.A can be fed through three methods.

- A power supply connected to header JP109 while header JP108 is used as ground reference;

- USB3 cable connected to USB3 receptacle connector J103;

3.3V VCC of PI3HDX1204E can be employed through three methods.

- The 3.3V generated from a DC-DC convertor U102;

- A power supply connected to header JP105 while header JP106 is used as ground reference;

- The 3.3V from a source connected to input DP connector J101 provided that header pin JP104 is shorted.

Figure 4: Power Circuit of PI3HDX1204E DP-to-HDMI Demo Board Rev.A

# Power Saving Mode

PI3HDX1204E can enter power saving mode by setting PRSNT# pin to high voltage level. In the schematic, PRSNT# pin is controlled by HPD pin from the sink device connected to J102 HDMI connector.

Figure 5: PRSNT# Circuit of PI3HDX1204E DP-to-HDMI Demo Board Rev.A

Alternatively, PRSNT# can be selected via switch SW101.

| PRSNT# | Pins 8 and 9 of SW101 | Output TMDS of PI3HDX1204E |
| --- | --- | --- |
| L | Short | Normal Mode |
| H | Open | Power Saving Mode |

Table 4: PRSNT# Setting of PI3HDX1204E DP-to-HDMI Demo Board Rev.A

# References

- High-Definition Multimedia Interface Specification Version 2.0, HDMI Forum, September 4, 2013

- High-Definition Multimedia Interface Version 2.0b Compliance Test Specification, HDMI Forum, May 16, 2014

- High-Definition Multimedia Interface Specification Version 1.4b, HDMI Licensing, LLC, October 11, 2011

- High-Definition Multimedia Interface Compliance Test Specification Version 1.4a, HDMI Licensing, LLC, March 4, 2010

# Appendix A: Demo Board Schematic

For clearer view of schematic diagram, please click the PDF file icon on the right.

# Text boxes

PI3HDX1204E

J102

DC-DC Convertor

USB3 Connector

Input Port

U102

ON/OFF Switch

J101

DP Input Connector

HDMI Output Connector

Output Port

U101

+3V3_SRC

J103

+5V_USB

+3V3_USB

SW101

U105

Power Distribution Switch

+3V3