PI3HDX1204E

PI3HDX1204E HDMI Application Information

Table of Contents

1	Introduction	2

2	EVB Schematic	2

2.1	Source Application	2

2.1.1	ESD Protectors on Output TMDS	2

2.1.2	Leakage Blockage for VOFF Test	3

2.2	Sink Application	4

2.2.1	ESD Protectors on Input TMDS	4

3	Layout Design Guideline	5

3.1	AC Coupling Capacitor	5

3.2	Differential Impedance (TDR)	5

3.3	Ground Via on Thermal Pad	6

4	Test Result	7

4.1	HDMI2.0 Test Setup	7

4.2	HDMI2.0 Trace Loss	7

4.3	HDMI2.0 Compliance Test Result of PI3HDX1204E EVB	8

4.4	HDMI1.4 Compliance Test Result of PI3HDX1204E EVB	9

5	References	9

# Introduction

PI3HDX1204E is a dual-mode DP level shifter and HDMI 2.0 linear re-driver. As HDMI data rate can be as fast as 6Gbps, signal integrity is critical. Typical application circuit, layout guideline and test setup are described in this application information.

# EVB Schematic

# Source Application

PI3HDX1204E is designed to accept AC-coupled as well as DC-coupled main link signals. When a dual-mode DP source is connected to the input of PI3HDX1204E in a source application, AC coupling capacitors must be placed at the input side.

Figure 1: PI3HDX1204E Source Application Circuit

# ESD Protectors on Output TMDS

As 8kV contact ESD is commonly required, ESD protectors are implemented at the output TMDS pins of PI3HDX1204E for source application. ESD8104 HDMI2.0 ESD protector can be considered to protect the 3.3V TMDS paths as its reverse working voltage is 3.3V.

http://www.onsemi.com/pub_link/Collateral/ESD8104-D.PDF

# Leakage Blockage for VOFF Test

When performing VOFF test specified in HDMI1.4a Compliance Test Specification, each output TMDS of PI3HDX1204E will be pulled to 3.3V via an external 50kΩ resistor. In this case, current will pass through an internal ESD protector at the output TMDS pin of PI3HDX1204E and leakage will be found at VDD pin of PI3HDX1204E.

Figure 2: HDMI1.4 VOFF Test Setup

Table 1: HDMI1.4 VOFF Requirement

To avoid this leakage, AP2151A power switch can be employed between the main 3.3V supply on a system and the VDD power plane of PI3HDX1204E. Below is an example borrowed from an evaluation board schematic.

Figure 3: Power Distribution Switch Example

# Sink Application

PI3HDX1204E can also be employed in a sink application as it offers a range of equalization setting.

Figure 4: PI3HDX1204E Sink Application Circuit

# ESD Protectors on Input TMDS

ESD protector selection guidance for source and sink applications is the same. Please refer to Section 2.1.1 for details.

# Layout Design Guideline

# AC Coupling Capacitor

Below is an example of placing AC coupling capacitors on high-speed channels.

Figure 5: AC Coupling Capacitor Placement

# Differential Impedance (TDR)

Layout guideline especially for high-speed transmission is critical. Please refer to PI3DPxxx_PI3HDxxx_Layout Guideline for detailed recommendations. Differential impedance test is required for both source and sink applications per HDMI2.0 specification.

Table 2: HDMI2.0 Differential Impedance Requirement for Source Application

Table 3: HDMI2.0 Differential Impedance Requirement for Sink Application

The PCB impedance immediately before and after an ESD protector must be adjusted to compensate the capacitance loading of the ESD protector. Below is an example designing RClampe0544M in PI3HDX1204E evaluation board. Trace impedances before and after the ESD protector are tuned to compensate the capacitance of RClamp0544M. Semtech’s layout guideline is followed.

https://www.semtech.com/images/promo/Layout_Guidelines_for_adding_ESD_Protection_in_HDMI.pdf

Figure 6: ESD Protector on PI3HDX1204E Source EVB

# Ground Via on Thermal Pad

At least eight ground vias are required on thermal pad of PI3HDX1204E. The recommended via size is 12/24 mil. Below is a reference for PI3HDX1204E ground pad.

Figure 7: Thermal Pad Design Example

# Test Result

# HDMI2.0 Test Setup

HDMI2.0 source test setup is available for evaluation and pre-test. Below is the internal HDMI2.0 test setup.

Figure 8: HDMI2.0 Test Setup

# HDMI2.0 Trace Loss

PI3HDX1204E is evaluated with the use of tailor-made FR4 trace cards as input traces plugged to the EVB.

| HDMI FR4 trace | 0 in | 6 in | 12 in | 18 in | 24 in | 30 in | 36 in |
| --- | --- | --- | --- | --- | --- | --- | --- |
| Insertion loss @ 6Gbps | -5.91 dB | -9.75 dB | -10.47 dB | -13.05 dB | -15.87 dB | -16.97 dB | -21.20 dB |

Table 4: HDMI2.0 FR4 Trace Loss

# HDMI2.0 Compliance Test Result of PI3HDX1204E EVB

# HDMI1.4 Compliance Test Result of PI3HDX1204E EVB

# References

- High-Definition Multimedia Interface Specification Version 2.0a, HDMI Forum, March 19, 2015

- High-Definition Multimedia Interface Specification Version 2.0h Compliance Test Specification, HDMI Forum, April 3, 2015

- High-Definition Multimedia Interface Specification Version 1.4b, HDMI Licensing, LLC, October 11, 2011

- High-Definition Multimedia Interface Compliance Test Specification Version 1.4a, HDMI Licensing, LLC, March 4, 2010

- SI05-03 Surging Ideas TVS Diode Application Note, Semtech, April 21, 2005