PI6C49X0210

PI6C49X0210 Demo Board User Manual
by Shengjiang Pan

Table of Contents

1	Introduction	2

2	Overview	2

3	Quick Start	4

4	Detail Description	5

5	Appendix A: PI6C49X0210 Demo Board Schematic	8

# Introduction

PI6C49X0210 is a high performance multi-voltage 10-outputs CMOS Fanout Buffer with internal Crystal Oscillator. PI6C49X0210 demo board is designed to demonstrate the performance and key features of PI6C49X0210. This user manual describes how to use this demo board. It will be divided into following sections:

- Overview

- Quick Start

- Detail Description

- Test Results

# Overview

Figure 1 is the block diagram of PI6C49X0210 demo board and Figures 2 is the top view of Demo board. Crystal, Ref0 and Ref1 can be selected as clock source input through JP1, JP2 and JP3. There are 10 output Jumpers for clock output test.

Figure 1: Block Diagram of PI6C49X0210 Demo Board

Figure 2: Top View of PI6C49X0210 Demo Board

# Quick Start

To start up the PI6C49X0210 demo board, complete the following steps:

- Ensure 5pf loadings are soldered at clock output header pins.

- Supply 3.3V to demo board at JP18 (Power) and JP19 (Ground).

- Place jumper at JP190.

- Set JP1 open: enable all clock outputs

- Set JP2 and JP3 open: Crystal is selected as source input.

| JP1 | JP2 | JP3 | JP190 |
| --- | --- | --- | --- |
| Open | Open | Open | Short |

Table 1: Jumpers Connection at Quick Start

Figure 3: Layout of PI3HDMI336 Demo Board (Top View)

# Detail Description

The functionality of Jumpers and key circuits are described in detail in this section.

  - Functionality of Jumpers

| Jumper | Description |
| --- | --- |
| JP1 | Output enable/disable: Short: disabled Open: enabled |
| JP2, JP3 | Selection of source input: JP2 JP3 Source selection Open Open Crystal Short Open Crystal Open Short Ref1 or Single End Short Short Ref0 or Single End |
| JP4, JP7, JP8, JP9, JP10, JP11, JP12, JP13, JP14, JP15 | Clock output test Jumpers |
| JP18 | Power pin |
| JP19 | Ground pin |
| JP190 | Power supply for Vddo: Open: Vddo does not connect to power supply. Short: Vddo connects to power supply. |

Table 2:  Function of Jumpers

  - Key Circuits Description

- Source Termination Circuit

33Ω source termination is placed more closed to IC within 0.1 inch to reduce reflection.

Figure 4: Termination at Clock Output

- Termination Circuit at Clock Input

PI6C49X0210 accepts single end clock or differential clock. If differential clock is as input, 100Ω termination should be soldered on the PCB; if single end clock is as input, 50Ω termination should be soldered on the PCB.

Figure 5: Termination at Clock Input

# Appendix A: PI6C49X0210 Demo Board Schematic

For more clear on viewing the schematic diagram, please click on this icon to open the PDF file.

# Text boxes

1’’

1’’

1’’

1’’

1’’

1’’

1’’

1’’

JP8

JP15

JP13

JP12

JP10

PIC49X0210

JP19

JP18

JP7

JP2

JP190

Ref 1

Ref 0

JP3

JP1

JP4

CLK4

CLK3

CLK2

CLK1

JP4

JP3

Crystal

JP14

JP11

JP9

JP1

CLK0

1’’

JP2

50Ω single end termination

100Ω differential termination

PI6C49X0210

1’’

Crystal

JP15

JP13

JP7

JP12

JP10

JP8

JP14

JP11

JP9

CLK5

CLK6

CLK7

CLK8

CLK9

Ref0

Ref1