## Slide 1
ZXCT213 PSpice
Model Validation Report
15/03/2024
Version 1.0

## Slide 2: ZXCT213
Version | Details | Author | Date | REMARKS
1.0 | PSpice Results | Sankalp | 15MAR2024 | Initial Release
Version History
2

## Slide 3: Contents
3
SL. NO. | CONTENTS | PG.NO
1. | Specs Compliance Matrix | 4-5
2. | Analysis Parameters | 6
3. | AC Analysis | 7-15
4. | Temperature Variation | 16-22
5. | DC Analysis | 23-31
6. | Transient Analysis | 32-40

## Slide 4: Spec Compliance Matrix
PARAMETER | SYMBOL | TEST CONDITION | DATASHEET VALUE |  |  | PSPICE VALUE | UNIT
 |  |  | Min | Typ | Max |  | 
Common-Mode Input | VCM | TA = -40°C to +125°C | -0.3 | -- | 26 | (-0.3)-26 | V
Common – Mode Rejection | CMRR | VIN+ = 0V to 26V, VSENSE = 0mV, TA = -40°C to +125°C | 100 | 120 | -- | 126 | dB
Offset voltage | VOS | VSENSE = 0mV | -- | +-0.55 | +-35 | +-100 | uA
Vos vs Temperature | dVos/dT | TA = -40°C to +125°C | -- | 0.1 | -- | 0.1 | uV/°C
Power supply rejection | PSRR | VS = 2.7V to 18V, VIN+ = 18V, VSENSE = 0mV | -- | +-0.1 | +-10 | +-0.1 | uV/V
Input bias current | IB | VSENSE = 0mV | -- | 28 | 35 | 28 | uA
Gain | G | -- | -- | 50 | -- | 49.77 | V/V

## Slide 5: Spec Compliance Matrix
PARAMETER | SYMBOL | TEST CONDITION | DATASHEET VALUE |  |  | PSPICE VALUE | UNIT
 |  |  | Min | Typ | Max |  | 
Gain Error | EG | A and B Version, VSENSE = -5mV to 5mV, TA = -40°C to +125°C | -- | +-0.03 | +-0.8 | +-0.46 | %
 |  | C Version, VSENSE = -5mV to 5mV, TA = -40°C to +125°C | -- | +-0.03 | +-0.8 | +-0.46 | 
Swing to V+ Power-supply Rail | VOH | RL = 10kΩ to GND, TA = -40°C to +125°C | -- | (V+)-0.05 | (V+)-0.2 | (V+)-0.05 | V
Swing to GND | VOL | RL = 10kΩ to GND, TA = -40°C to +125°C | -- | (VGND)+0.005 | (VGND)+0.05 | (VGND)+0.005 | V
Operating voltage range | VS | TA = -40°C to +125°C | 2.7 | -- | 26 | 2.7-26 | V
Quiescent Current | IQ | VSENSE = 0mV | -- | 65 | 100 | 65 | uA

## Slide 6: Analysis Parameter
6
Parameter | Value
VNTOL | 5u
ABSTOL | 1n
CHGTOL | 1p
ITL4 | 40
TIME STEP | 10n
Note: Remaining parameters are set to the default values of Allegro Pspice 17.4.

## Slide 7
AC Analysis

## Slide 8: Frequency Response Test Setup and Condition
VIN
Testbench Description
  The above testbench has been set-up to observe the frequency response of the device.
  Keep AC=1 : For AC analysis; Keep AC=0 : For transient analysis.
  Time taken for the simulation to complete which runs for the frequency range of 10Hz to 10MHz = Few seconds.
Test Condition: VSUPPLY=5V, VREF=2.5V, FREQ=10Hz – 10MHz

## Slide 9: PSpice Simulation Result / Datasheet
P-Spice Result

## Slide 10: Gain Error Test Setup and Condition
VIN
Testbench Description
  The above testbench has been set-up to observe the frequency response of the device. The Error is inducted in the device by changing the values of the source resistors, RS1 & RS2
  Keep AC=1 : For AC analysis; Keep AC=0 : For transient analysis.
  Time taken for the simulation to complete which runs for the frequency range of 10Hz to 10MHz = Few seconds.
Test Condition: VSUPPLY=5V, VREF=2.5V, FREQ=10Hz – 10MHz

## Slide 11: PSpice Simulation Result
When Rs(=5Ω) is connected,
Gain = 33.94 dB = 49.77 V/V
When Rs (=5Ω) is not connected, Gain = 33.97 dB = 50 V/V
Therefore, the Gain Error =
{(50 – 49.77)/50}*100 = 0.46%

## Slide 12: PSRR Test Setup and Condition
VIN
Testbench Description
  The above testbench has been set-up to observe the PSRR characteristics of the device.
  Keep AC=1 : For AC analysis; Keep AC=0 : For transient analysis.
  Time taken for the simulation to complete which runs for the frequency range of 10Hz to 100KHz = Few seconds.
Test Condition: VSUPPLY=5V, VREF=2.5V, FREQ=10Hz – 100kHz

## Slide 13: PSpice Simulation Result / Datasheet
P-Spice Result
Datasheet

## Slide 14: CMRR Test Setup and Condition
IL
VIN
ILED
Testbench Description
Test Condition: VSUPPLY=5V, VREF=2.5V, FREQ=10Hz – 1MHz
  The above testbench has been set-up to observe the CMRR vs frequency response of the device.
  Keep AC=1 : For AC analysis; Keep AC=0 : For transient analysis.
  Time taken for the simulation to complete which runs for the frequency range of 10Hz to 1MHz = Few seconds.

## Slide 15: PSpice Simulation Result / Datasheet
P-Spice Result
Datasheet

## Slide 16
Temperature variation

## Slide 17: Quiescent current vs Temperature
VIN
Testbench Description
  The above testbench has been set-up to observe the variation of the Quiescent current with respect to temperature variation.
  Time taken for the simulation to complete = Few seconds.
Test Condition: VSUPPLY=2.7V, VREF=2.5V, COMMON MODE VOLTAGE (V_CM)=5V

## Slide 18: PSpice Simulation Result / Datasheet
P-Spice Result
Datasheet

## Slide 19: Offset voltage vs Temperature
VIN
Testbench Description
  The above testbench has been set-up to observe the variation of the Offset voltage with respect to temperature.
  Time taken for the simulation to complete = Few seconds.
Test Condition: VSUPPLY=2.7V, VREF=0, V(IN+)=0

## Slide 20: PSpice Simulation Result / Datasheet
P-Spice Result
Datasheet

## Slide 21: CMRR vs Temperature
VIN
Testbench Description
  The above testbench has been set-up to observe the variation of CMRR with respect to temperature.
  Keep AC=1 : For AC analysis; Keep AC=0 : For transient analysis.
  Time taken for the simulation to complete = Few seconds.
Test Condition: VSUPPLY=5V, VREF=2.5, V(IN+)=12V

## Slide 22: PSpice Simulation Result / Datasheet
Datasheet

## Slide 23
DC Analysis

## Slide 24: Bias Current Test Setup 1 and Condition
VIN
Testbench Description
  The above testbench has been set-up to observe the variation of the input bias current with respect to the common mode voltage variation.
  Time taken for the simulation to complete = Few seconds.
Test Condition: VSUPPLY=2.7V, VREF=2.5V, COMMON MODE VOLTAGE (V_CM)=5V

## Slide 25: PSpice Simulation Result / Datasheet
P-Spice Result
Datasheet
Internal nodes are plotted to avoid the effect of loop resistors.
ABM213: Non inverting; ABM214: Inverting

## Slide 26: Bias Current Test Setup 2 and Condition
VIN
Testbench Description
  The above testbench has been set-up to observe the variation of the input bias current with respect to the common mode voltage variation.
  Time taken for the simulation to complete = Few seconds.
Test Condition: VSUPPLY=0V, VREF=2.5V, COMMON MODE VOLTAGE (V_CM)=5

## Slide 27: PSpice Simulation Result / Datasheet
P-Spice Result
Datasheet
Internal nodes are plotted to avoid the effect of loop resistors.
ABM213: Non inverting; ABM214: Inverting

## Slide 28: Bias Current Test Setup 3 and Condition
VIN
Testbench Description
  The above testbench has been set-up to observe the variation of the input bias current with respect to the common mode voltage variation.
  Time taken for the simulation to complete = Few seconds.
Test Condition: VSUPPLY=2.7V, VREF=0V, COMMON MODE VOLTAGE (V_CM)=5V

## Slide 29: PSpice Simulation Result / Datasheet
P-Spice Result
Datasheet
Internal nodes are plotted to avoid the effect of loop resistors.
ABM213: Non inverting; ABM214: Inverting

## Slide 30: Bias Current Test Setup 4 and Condition
VIN
Testbench Description
  The above testbench has been set-up to observe the variation of the input bias current with respect to the common mode voltage variation.
  Time taken for the simulation to complete = Few seconds.
Test Condition: VSUPPLY=0V, VREF=0V, COMMON MODE VOLTAGE (V_CM)=5V

## Slide 31: PSpice Simulation Result / Datasheet
P-Spice Result
Datasheet
Internal nodes are plotted to avoid the effect of loop resistors.
ABM213: Non inverting; ABM214: Inverting

## Slide 32
Transient Analysis

## Slide 33: Offset voltage test setup
VIN
Testbench Description
  The above testbench has been set-up to observe the offset voltage of ZXCT213 A, B & C version. Parameter “VERSION” is used to control the A(VERSION=1), B(VERSION=2), C(VERSION=3) versions.
  Keep AC=1 : For AC analysis; Keep AC=0 : For transient analysis.
  Time taken for the simulation to complete = Few seconds.
Test Condition: VSUPPLY=2.7V, VREF=0V

## Slide 34: PSpice Simulation Result / Datasheet
P-Spice Result
Version | Datasheet Value | PSPICE Value
ZXCT213A | 100uV | 104uV
ZXCT213B | 90uV | 94uV
ZXCT213C | 90uV | 94uV
ZXCT213A
ZXCT213B/C

## Slide 35: Common Mode Voltage Vs Transient Response Test Setup and Condition
VIN
Testbench Description
  The above testbench has been set-up to observe the transient response in case of common mode voltage.
  Keep AC=1 : For AC analysis; Keep AC=0 : For transient analysis.
  Time taken for the simulation to complete = Few seconds.
Test Condition: VSUPPLY=2.7V, VREF=200mV, COMMON MODE VOLTAGE (CM)=0V-5V-0V

## Slide 36: PSpice Simulation Result / Datasheet
P-Spice Result
Datasheet

## Slide 37: Non Inverting Differential Input Overload Test Setup and Condition
VIN
Testbench Description
  The above testbench has been set-up to observe the response in non inverting input overload.
  Keep AC=1 : For AC analysis; Keep AC=0 : For transient analysis.
  Time taken for the simulation to complete = Few seconds.
Test Condition: VSUPPLY=5V, VREF=2.5V, Input Voltage=0V-10V-0V

## Slide 38: PSpice Simulation Result / Datasheet
P-Spice Result
Datasheet

## Slide 39: Inverting Differential Input Overload Test Setup and Condition
VIN
Testbench Description
  The above testbench has been set-up to observe the response in inverting input overload.
  Keep AC=1 : For AC analysis; Keep AC=0 : For transient analysis.
  Time taken for the simulation to complete = Few seconds.
Test Condition: VSUPPLY = 5V, VREF = 2.5V, Input Voltage = 0V-10V-0V

## Slide 40: PSpice Simulation Result / Datasheet
P-Spice Result
Datasheet

## Slide 41
THANK YOU